## Slide 1: Testbed for Validating Second-Generation TDI and Clock Noise Correction for LISA
Karin Kruuse
Reid Ferguson, Patrick Krieger, Daniele Vetrugno, Guido Müller
Notes: Hi! I’m Karin Kruuse. I’m a first year PhD student at the albert Einstein Institute in Hannover and I’ll be talking about the LISA testbed we are building there.

## Slide 2
Notes: So to those who need a reminder, LISA is an ESA led mission to put a gravitational wave detector in space to detect mHz GWs without the Newtonian noise we have here on Earth.

## Slide 3: The LISA Satellites
Jennrich, 2010
Split interferometry
Unequal arm lengths and laser frequency noise
Heterodyne interferometry
Notes: For this ambitious goal, the iconic triangular constellation will trail Earth on a heliocentric orbit. Due to not perfect orbits, the arm lengths are unequal which leads to the biggest noise contribution for LISA signals which is the laser noise. The arm lengths are also time varying which results in Doppler shifts on the inter-satellite laser fields. For LISA heterodyne interferometry is used – meaning the interfering light fields have slightly – MHz – different carrier/central frequencies and the resulting reading from the photodetector will oscillate at the frequency of said difference. This is what we call the beatnote.
From the intersatellite measurement we derive the distance between the spacecraft.
Now, in addition to the intersatellite light fields, the LISA satellites include interferometric measurements between two sources on the same satellite to measure the distances from the spacecraft to each of the test masses. This is often referred to as split interferometry for LISA.

## Slide 4: LISA Interferometric Metrology System
Test mass
Optical bench
Far spacecraft
Adjacent laser
Local laser
USO
USO – Ultra Stable Oscillator
– science beat note
– test mass beat note
– reference beat note
Notes: So here we see a simple illustration of one of the optical benches on a LISA satellite.

## Slide 5: LISA Interferometric Metrology System
Test mass
Optical bench
Far spacecraft
Adjacent laser
Local laser
USO
USO – Ultra Stable Oscillator
– science beat note
– test mass beat note
– reference beat note

## Slide 6: LISA Interferometric Metrology System
Test mass
Optical bench
Far spacecraft
Adjacent laser
Local laser
USO
USO – Ultra Stable Oscillator
– science beat note
– test mass beat note
– reference beat note
Notes: Add references to other experiments

## Slide 7: LISA Interferometric Metrology System
Test mass
Optical bench
Far spacecraft
Adjacent laser
Local laser
USO
USO – Ultra Stable Oscillator
– science beat note
– test mass beat note
– reference beat note
Notes: Add references to other experiments

## Slide 8: LISA Interferometric Metrology System
Test mass
Optical bench
Far spacecraft
Adjacent laser
Local laser
USO
USO – Ultra Stable Oscillator
– science beat note
– test mass beat note
– reference beat note
Notes: Add references to other experiments

## Slide 9: Laser Noise Reduction via TDI
Hartwig, 2021
Time Delay Interferometry (TDI) is a cluster of methods to construct virtual equal arms in post-processing.
Transponder signal
Synthesized transponder signal
Notes: Add more generations, or like illustrate how you get to TDI 1 and 2

## Slide 10: Clock Noise Reduction
Lisa metrology system-final report, 2014
After demodulation, considering laser noise and clock jitter:

## Slide 11: Previous Experiment
Mitryk, 2012
Strain amplitude 4.35×10−20 m/m
TDI 1.0
TDI 2.0
Notes: Decades ago a testbed was build in University of Florida. Our design, which i will soon enough get to, was very similar to ours – so it is the predecessor to our testbed. The experiments performed were able to show that with TDI it is infact possible to cancel the laser noise orders of magnitude while preserving the gravitational wave signal. The strain used here is about two orders of magnitude higher that what was expected for LISA though. Overall the testbed was largely limited by the technology of the time – the baseline noise was high and the possibilities with adding GWs were limited. The testbed also didnt include the laserfield modulation for clock noise removal.

## Slide 12: miniLISA
miniLISA is a hardware testbed that aims to simulate LISA’s signal chain and test whether we can recover a gravitational wave signal from a realistic, noisy system.
To start with, we want to test the combination of second generation TDI and the clock noise removal post-processing methods on experimental data.
miniLISA could also offer a substitute to modelled noise sources included in current data analysis.
Optical input
Optical input
Delay
+ GW
Phasemeter
electrical signal
electrical signal

## Slide 13: Current Status
A fully electronic implementation of the interferometry system together with a delay and gravitational wave injection has already been developed and is being tested.
Time varying delays
Doppler shifts for both the carrier and sidebands
Gravitational wave injection
AMD Zynq™ UltraScale+™ RFSoC ZCU208 Evaluation Kit
Notes: DIAGRAM!

## Slide 14: One-arm Phase Measurement
Set up for generating one LISA-like arm link.
Sci IF
Red Pitaya based LISA
Notes: typo

## Slide 15
Two-arm Testbed
Notes: I have to remake this shit

## Slide 16: Prospects and Conclusions
miniLISA will replicate the LISA system in a lab for playthrough of data post-processing
At the core of miniLISA is the delay line which is
Addition of a third arm connection for better parameter estimation and data analysis
More elaborate clocking distribution system to better replicate LISA

## Slide 17
Thank you for listening!