## Slide 1: Testbed for Validating Second-Generation TDI and Clock Noise Correction for LISA
Karin Kruuse
Reid Ferguson, Daniele Vetrungo, Guido Müller
Notes: Date. Change
Add event, location, student seminar intro talk

## Slide 2: Outline of the Talk
LISA interferometry
About previous LISA simulators
Overview of our proposed LISA testbed
  Its purpose and goals
  Status of the current purely electronic testbed
  Putting together an optical input
Notes: studying the realistic clock noise pipeline

## Slide 3: The Satellites
Jennrich, 2010
Three satellites surrounding six test masses in free fall
Each satellite houses two lasers, two optical benches and a phasemeter.
Each optical bench houses three interferometers.
The test mass to test mass distances are measured in three parts – this is the so-called split interferometry used in LISA.
Notes: Maybe just bullet points/ or just read only if that helps with nerves

## Slide 4: Internals of a LISA Spacecraft
heterodyne interferometry
LISA interferometric metrology system
Notes: UGLY

## Slide 5: Laser Noise Reduction via TDI
Hartwig, 2021
0th generation TDI X combination, equal unchanging arm lengths
In practice, 2nd generation combinations should suppress noise enough to meet the requirement.
Time Delay Interferometry (TDI) is a cluster of methods to construct virtual equal arms in post-processing.

## Slide 6: Clock Noise Reduction
Lisa metrology system-final report, 2014
After demodulation, considering laser noise and clock jitter:
Notes: FIX MATH

## Slide 7: Previous Experiments
De Vine et al., 2010: Experimental Demonstration of Time-Delay Interferometry for LISA, JPL
Vidal, 2023: Validation expérimentale des performances interférométriques de LISA, Paris
Laser noise, Clock jitter, No delay
Laser noise, Clock Jitter, Delay
Mitryk, 2012: Laser Noise Mitigation through Time Delay Interferometry for Space-based Gravitational Wave Interferometers Using the UF Laser Interferometer
Laser noise, No Clock Jitter, Realistic Delay

## Slide 8: MiniLISA
MiniLISA is a hardware testbed that aims to simulate LISA’s signal chain and test whether we can recover a gravitational wave signal from a realistic, noisy system.
To start with, we want to test the combination of second generation TDI and the clock noise removal post-processing methods on experimental data.
MiniLISA could also offer a substitute to modelled noise sources included in current data analysis.
Notes: Expand on the goals more

## Slide 9: Current Status
A fully electronic implementation of the interferometry system together with a delay and gravitational wave injection has already been developed and is being tested.
Time varying delays
Doppler shifts for both the carrier and sidebands
Gravitational wave injection

## Slide 10: The Delay Line
The center of the experiment is the delay line.
The added varying delays, gravitational wave signals and Doppler shifts are controllable via a Python-based interface.
AMD Zynq™ UltraScale+™ RFSoC ZCU208 Evaluation Kit

## Slide 11: Signal Processing on the Delay Line
The evaluation board includes enough to take in two photodetector readings and output the corresponding LISA-like beatnote as an electrical signal.
Credit: Reid Ferguson

## Slide 12: Delay Line Noise Measurement
Credit: Reid Ferguson

## Slide 13: Phase Measurement with an Optical Input
Set up for generating one LISA-like science interferometer readout.
Notes: typo

## Slide 14: Phase Measurement with an Optical Input
Set up for generating one LISA-like science interferometer readout.
Sci IF
Notes: Add the beatnotes here?

## Slide 15: Phase Measurement with an Optical Input
Set up for generating one LISA-like arm link.
~10 MHz
~60 MHz
~15 MHz
Notes: typo

## Slide 16: The Phasemeters
Red Pitaya running LISA gateware
Red Pitaya

## Slide 17
Two-arm Testbed
Notes: Here have the reference

## Slide 18
Two-arm Testbed

## Slide 19: Possible Additions
More true-to-LISA clock noise transfer
  Needs some more studying
Third arm link
  Needs frequency planning
Test mass acceleration noise
Notes: Firstly, the actual clock transfer system is a bit more complicated than just USO – phase modulation – read out on other SC.

## Slide 20
Thank you for listening!