## Slide 1: Testbed for Validating Second-Generation TDI and Clock Noise Correction for LISA
Karin Kruuse, Reid Ferguson, Sourath Ghosh, Patrick Krieger, Daniele Vetrugno, Guido Mueller Max Planck Institute for Gravitational Physics/Leibniz University Hannover
Notes: This is a status report

## Slide 2: LISA Science Interferometer
Two primary noises in the LISA raw data – laser noise and clock timing jitter
Notes: Stress that we want to replicate these noise couplings for the carrier or inter-spacecraft interferometer
Mention the reason for the testbed
Clarify the goal of the testbed more? Like our results are results for TDI. In best case scenario we just show that simultaions are fine

## Slide 3: LISA Science Interferometer
Two primary noises in the LISA raw data – laser noise and clock timing jitter
Notes: Stress that we want to replicate these noise couplings for the carrier or inter-spacecraft interferometer
Mention the reason for the testbed

## Slide 4: Replicating the LISA Arm in the Lab
LISA arm
Testbed arm

## Slide 5: Replicating the LISA Arm in the Lab
Carrier from 281 THz to ~50MHz
LISA arm
Testbed arm

## Slide 6: Replicating the LISA Arm in the Lab
Inter-satellite interferometers
LISA arm
Testbed arm
Notes: Mention delayline was talked about! That’s our starting point. Transition from eletronic to opto electronic (add somewhere)

## Slide 7: Replicating the LISA Arm in the Lab
LISA arm
Testbed arm
Notes: Fix the signs

## Slide 8: Full Testbed
Notes: Lasers, delaylines, locking, add pic of lab

## Slide 9: Full Testbed
Notes: CAVITY

## Slide 10: Cavity Locking
Two lasers locked to separate cavities – 25 cm and 30 cm
Two separate Pound-Drever-Hall (PDH) locks
Beat note needs to be below 60 MHz
Illustrative cavity resonances
Notes: The length variability, like how it affects the

## Slide 11: Delay Line
Time varying delays
Doppler shifts for both the carrier and sidebands
Gravitational wave injection
AMD Zynq™ UltraScale+™ RFSoC ZCU208 Evaluation Kit
Intrinsic noise floor of one board in purple
Notes: Change the benchmark?

## Slide 12: PLL Lock of Far Spacecraft
Photodetector readings are dominated by free running laser frequency noise.
Mixed output is orders of magnitude lower.
Notes: like its actually measured. Make the diagram more acurat – split the PLL and the phasemeter (like actually the details of the signals moving, especially the purple)

## Slide 13: PLL Lock of Far Spacecraft
We can recover a LISA-like one-way laser noise transfer function
Notes: Explain the extraction clearly, fix the mistake or remove the second ratio

## Slide 14: Clock Noise in LISA
Notes: Clarify the modulating freq.
Add clarifing notes for the terms/frequencies (already in previous slides)

## Slide 15: Replicating the LISA Arm in the Lab
LISA arm
Testbed arm
Notes: Highlight the modulation frequency in the text, explain the GHz limitation better change slide text, this is sideband

## Slide 16: Clock Tone Transfer Performance
Modulator noise and the intrinsic noise of the delay line board are too loud if MHz modulation is used.

## Slide 17: GHz Modulation -- Solution 1
Where to derive the modulating tone from?
Heterodyned sideband beat notes add a new timing jitter to the mix.
Notes: Solution nr 1

## Slide 18: GHz Modulation -- Solution 2
Mixing of a GHz signal in the ADC – effectively increasing the bandwidth of the input of the electronics.
Notes: Our firmware currently doesn’t allow for GHz “front end”. Solution nr 2, add Clarify the solution properly. Like why is this even an issue currently

## Slide 19: Conclusions and Next Steps
✓ Delay line — working, below requirement
✓ PLL lock demonstrated with free running lasers
○ Assembling the optical layout and cavities
○ GHz sideband chain — under investigation
○ Delay board clock noise removal
○ Ranging — in development
○ Full TDI and clock noise removal
Thank you!
Notes: Fix the clock noise stuff
Add the cavity locking plans? – how u get the good beatnote (in the right range)
Take out delay line stuff, like put them together

## Slide 20: Modulation Noise Characterization
Notes: Add fibers?

## Slide 21: What to do with the clock noise?
We are working on another layer of post processing remove this noise
Can be done after TDI and LISA-like clock noise removal
Tests of Delay Line Board Clock Phase Noise
Only if the residuals are added
And rhen other noises should also be added
Notes: Add something that indicates the residuals

## Slide 22: Experiments so Far
A new baseline measurement with an optical signal and free running delay line board clock reveals a potential problem.
Tests of Delay Line Board Clock Phase Noise
Notes: Take out

## Slide 23: Experiments so Far
R. Ferguson et al., Applying TDI to Hardware-Simulated Data, 2025
Fully electronic tests of TDI.
Notes: Update! If shown, show later

## Slide 24: Predecessor Testbed
Strain amplitude 4.35×10−20
TDI 1.0
TDI 2.0
Results from University of Florida Laser Interferometry Simulator
Credit: Mitryk, 2012
Notes: Decades ago a testbed was build in University of Florida. Our design, which i will soon enough get to, was very similar to ours – so it is the predecessor to our testbed. The experiments performed were able to show that with TDI it is infact possible to cancel the laser noise orders of magnitude while preserving the gravitational wave signal. The strain used here is about two orders of magnitude higher that what was expected for LISA though. Overall the testbed was largely limited by the technology of the time – the baseline noise was high and the possibilities with adding GWs were limited. The testbed also didnt include the laserfield modulation for clock noise removal.

## Slide 25: LISA Laser Frequency Noise
Credit: Jennrich, 2010
Unequal arm lengths and laser frequency noise
As per LISA requirements
Hence for the arm length uncertainty we get
But to be sensitive enough to detect GWs, we need